## Slide 1
THESIS PROTOTYPE
On-device AI for construction reporting
Phase 1-4 implementation, testing, model selection, and local extraction architecture
01
ASR FOUNDATION
audio capture, VAD, engine registry
02
MANUAL ASR TESTS
40 EN/FI cases across 3 noise sessions
03
NATIVE IOS PATH
configurable Apple Speech, metrics, privacy policy
04
LOCAL EXTRACTION
Qwen GGUF + deterministic validation
01

## Slide 2
PRESENTATION PLAN
The deck follows the prototype as it matured from audio capture to validated task drafts.
Phase 1
Implementation foundation
Record or stream speech, configure audio, route engines, capture timing metrics.
>
Phase 2
Manual testing tool
Run controlled EN/FI construction sentences across quiet, moderate, and hard noise.
>
Phase 3
Selected ASR path
Advance Native iOS ASR because the reporting workflow needs live feedback.
>
Phase 4
Local LLM extraction
Convert transcript into a safe General Task Form draft with local data grounding.
What is deliberately not shown as achieved: numeric aggregate ASR rankings, Apple ASR fine-tuning, custom noise removal, cloud LLM calls, embeddings/vector search, GPS/photos/task submission.
Source: local prototype docs and implementation files
02

## Slide 3
PHASE 1 IMPLEMENTATION
Phase 1 built the ASR foundation before any extraction logic existed.
Microphone
expo-audio or PCM live stream
>
Audio contract
16 kHz, mono; WAV/PCM on iOS
>
VAD layer
energy threshold and segment buffering
>
ASR engine
Native, Whisper, Qwen path
>
Result object
standard TranscriptionResult
>
Local storage
asr-results/results.json
VAD is segmentation, not streaming
VAD closes speech segments for offline engines; it does not create partial-token streaming.
One result schema
Every attempt stores model, language, runtime mode, durations, TTFS, transcript, segments, sample rate, audio URI, and errors.
Failure is data
Unsupported or missing-model attempts are saved instead of crashing the test flow.
Sources: phase-1 doc, useAsrController.ts, vadService.ts, asr.types.ts
03

## Slide 4
PHASE 1 AUDIO SIZE
The audio path is sized around 16 kHz mono PCM, so every segment is predictable.
Input unit
Implemented value
Size implication
Why it matters
Sample rate
16,000 samples/sec
1 second = 16,000 samples
Matches Whisper, Qwen/VAD, and mobile ASR test contract.
Channels
1 channel mono
No stereo doubling
Keeps memory and model input simple.
PCM bit depth
16-bit linear PCM WAV on iOS
1 second ~= 32 KB raw PCM
Avoids compressed recorder output for Whisper.
VAD frame
30 ms
480 samples ~= 960 bytes
Small enough for responsive speech/silence detection.
Pre-speech pad
200 ms
3,200 samples ~= 6.4 KB
Preserves speech onset before threshold crossing.
Max VAD segment
12,000 ms
192,000 samples ~= 384 KB
Caps offline segment size for Qwen-style simulated streaming.
Whisper window
30 seconds internally
480,000 samples ~= 960 KB
Still used as full-recording transcription, not live partial streaming.
Audio options: .wav, 16 kHz, mono, iOS LINEARPCM, 16-bit, little-endian, non-float. Android keeps the Expo high-quality m4a path.
Sources: audioHelpers.ts, vadService.ts, phase-1 doc
04

## Slide 5
PHASE 1 RUNTIME MODES
The prototype reports what each engine really does instead of pretending every model streams.
Engine
Runtime mode
Role in prototype
Important caveat
Native ASR
true-streaming when partial callbacks work
Real-time mobile baseline
Availability and on-device support vary by OS, locale, and device.
Whisper base
offline-full-recording
Multilingual offline baseline
Transcribes after recording stops; no live partial-token path in this app.
Qwen3-ASR
vad-segmented-offline
Advanced on-device candidate
Requires Sherpa model files; text appears after VAD utterance boundaries.
Runtime mode is thesis evidence
Every saved row carries true-streaming, vad-segmented-offline, offline-full-recording, or unsupported.
Unsupported is explicit
Missing model files produce saved unsupported/error rows with model and test metadata.
Metrics travel with the result
TTFS, transcription time, speech/silence duration, segments, and sample rate are preserved.
Sources: phase-1 doc, ASR engine registry/types
05

## Slide 6
PHASE 2 TESTING
Phase 2 turned the app into a controlled manual ASR testing tool.
Test case
Reference sentence, language, category, difficulty, expected fields.
40 cases across English and Finnish.
Test session
Noise condition, target dBA range, device, noise source, measurement notes.
3 default sessions.
Test result
Recognized text, WER/CER, timings, runtime mode, success/error, device feasibility fields.
>
>
Session
Noise condition
Target dBA
Purpose
S00_QUIET_UNDER_50DBA
quiet
35-50
Baseline speech recognition.
S01_MODERATE_65_75DBA
moderate_noise
65-75
Construction-like interference.
S02_HARD_80_85DBA
hard_noise
80-85
Stress test for reporting feasibility.
Sources: phase-2 doc and phase2_manual_asr_testing_config_en_fi.json
06

## Slide 7
PHASE 2 METRICS
The scoring layer converts a spoken test into a comparable research row.
Normalize
lowercase, trim, collapse spaces, remove basic punctuation while preserving letters/digits such as A302
WER
Levenshtein distance over normalized word tokens divided by reference word count
CER
Levenshtein distance over normalized characters excluding whitespace
Latency
TTFS from first observed text, transcription time, recording duration, real-time factor
Export
CSV joins test case + session + result into one analyzable file
Phase 2 keeps battery, thermal, and memory fields in the schema even when the device cannot provide them yet. That preserves room for later feasibility analysis without blocking manual ASR testing.
Sources: asrScoring.ts, manualAsrResultBuilder.ts, phase-2 doc
07

## Slide 8
PHASE 2 TO PHASE 3
Native iOS ASR was selected because the reporting workflow needs live mobile feedback.
Candidate
Phase 2 fit
Selection signal
Phase 3 decision
Native iOS ASR
Live partial/final text in the mobile flow
Best current fit in the iPhone 11 Pro manual pilot for fast reporting interaction
Advance this path first.
Whisper base
Reliable offline multilingual baseline
Useful comparison model, but full-recording flow delays feedback
Keep as benchmark.
Qwen3-ASR
Potential local advanced model
Depends on local Sherpa model files; simulated streaming after VAD boundaries
Keep as candidate.
Parakeet
Available only when configured
Comparison path, not the selected Phase 3 implementation target
Do not optimize first.
Important thesis wording: Phase 3 does not fine-tune Apple's ASR model. It improves how Native iOS ASR is configured, observed, measured, and integrated into the prototype.
Sources: phase-3 doc; no committed aggregate WER/CER CSV was found
08

## Slide 9
PHASE 3 SELECTION LOGIC
The selected model path was improved around the workflow, not by retraining the recognizer.
Phase 2 evidence
Manual pilot showed Native iOS best fit for live iOS reporting.
Workflow need
User speaks on site and sees feedback before moving to extraction.
Selected path
Native iOS ASR becomes the Phase 3 focus.
Improvement scope
Configure, measure, preserve raw transcript, and log capabilities.
>
>
>
Custom Expo native module
Exposes Apple Speech request configuration React Native could not access.
Contextual strings scaffold
Up to 90 short construction terms, split EN/FI, disabled by default.
Punctuation scaffold
iOS 16+ addsPunctuation toggle, measured separately from WER/CER.
On-device policy
prefer / require / allowNetwork with capability checks and privacy mode logging.
Pause-aware accumulator
Preserves earlier phrases when Apple Speech revises text after pauses.
Sources: phase-3 doc, Native ASR Phase 3 types
09

## Slide 10
PHASE 3 NATIVE ARCHITECTURE
React Native owns the experiment; Swift owns Apple Speech.
Phase 3 UI
language, session, toggles, save/export
NativeASR config
locale, policy, context, punctuation
TS bridge
nativeIOSASRModule.ts
Swift module
NativeIOSASRModule.swift
Apple Speech
SFSpeechRecognizer
>
>
>
>
Events back to UI
onPartialResult, onFinalResult, onMetrics, onError, onState
Result builder
raw, normalized, improved transcript and WER/CER
Local storage + CSV
phase3-native-ios-asr export
events
Sources: phase-3 doc, nativeIOSASRModule.ts, NativeIOSASRModule.swift
10

## Slide 11
PHASE 3 IMPROVEMENTS
Phase 3 made Native iOS ASR configurable, observable, and defensible.
Locale control
en-US / fi-FI are sent to SFSpeechRecognizer so availability and support are device-locale specific.
On-device policy
prefer, require, or allowNetwork. The module checks support before forcing offline recognition.
Contextual strings
45 English + 45 Finnish construction phrases, enabled only for controlled experiments.
Punctuation
addsPunctuation is logged separately because readability can improve even when normalized WER is unchanged.
Transcript accumulation
Partial revisions after pauses append to committed transcript instead of wiping earlier speech.
Observability
TTFS, final latency, RTF, privacy mode, audio session, recognizer capability, success/error.
This is a measured configuration improvement. It does not claim Apple model fine-tuning, custom denoising, or guaranteed offline recognition.
Sources: phase-3 doc and Native ASR Phase 3 types
11

## Slide 12
PHASE 4 PURPOSE
Phase 4 begins the transition from transcript to General Task Form draft.
Phase Objective
Creates a partial Congrid-style General Task Form draft from transcript, local reference data, and a controlled local LLM.
User role
The user reviews, edits, confirms, or rejects values before any future final form flow.
13

## Slide 13
PHASE 4 ARCHITECTURE
The LLM suggests, the validator decides, and the user confirms.
Phase 3 transcript
raw or improved text
>
Transcript prep
trim/select source
>
Reference data
companies, tags, actions, due dates
>
Candidate resolver
local rule/responsibility matching
>
LLM input + prompt
allowed values + candidates
Provider
mock or local Qwen GGUF
>
Raw JSON text
structured extraction output
>
Safe parser
fences, JSON, formId, fields
>
Draft validator
allowed values only
>
Result + UI
draft, review suggestions, CSV
controlled JSON extraction
v1 safety boundary: no unsupported values enter final fields
Sources: phase-4 complete technical report
14

## Slide 14
PHASE 4 LOCAL MODEL
Qwen2.5 1.5B Instruct Q4_K_M is the first practical local extraction model.
Selected model
Qwen2.5-1.5B-Instruct-GGUF
Q4_K_M quantization
GGUF format
Runtime target
llama.rn binding to llama.cpp-compatible local runtime inside custom Expo dev build
Model storage
<documentDirectory>/models/llm/qwen2_5_1_5b_instruct_q4_k_m/*.gguf
Git policy
models/llm/**/*.gguf ignored
>
>
>
Runtime setting
Current value
Reason for baseline
n_ctx
4096
Enough prompt room for transcript, allowed values, candidates, policy, and JSON shape.
n_gpu_layers
99
Use available device acceleration through llama.rn where supported.
n_predict
700
Baseline cap before compact-output tuning.
temperature/top_p
0 / 1
Deterministic structured extraction.
Sources: phase4ModelConfig.ts, phase4LocalLLMProvider.ts
15

## Slide 15
PHASE 4 VALIDATION
Validation rebuilds the final draft from local allowed data, not from model trust.
Company
Only allowed local company IDs/names enter final field. Invented names become review context.
Area
Filled only when spoken and allowed or candidate-derived; generic bathroom is rejected.
Action
Only configured required actions are written.
Due date
Only Now, +3 days, +7 days; tomorrow stays review-only.
Tags
Allowed tags only; invented tags removed.
Fixed fields
list=Hallo, marker manual, photos skipped, impacts not configured, notifications=false.
Example: if the transcript says 'gas connection tomorrow', the draft can suggest a plumbing company and Korjaus, but due date remains manual/null while 'tomorrow' is preserved in reviewSuggestions.
Sources: phase4DraftValidator.ts, phase-4 complete technical report
16